## Slide 1: Durable and Handy External Plastic Pivot Hinge with DfAM
20151229 Chanyoung Park

## Slide 2
Our target is door in our house bathroom. Usually, door hinges are made of steel material, but it is exposed outside. If you look at the bathroom in your house, you can see that the hinge is rusted.
Also, these are very difficult to install because they need to be installed between a door and a frame.
Water
other matter
Durable and Handy Plastic Pivot Hinge !!!!!
Problem Description

## Slide 3: Goal and Solution
First
it must be resistant to
deformation by foreign materials.
Second
it should be a design that is easy to install when replacing hinge.
Third
it must be simple and aesthetically free in design.
Plastic Hinge
Pivot Hinge
Minimal Structure
Our Solution
Durable and Handy Plastic Pivot Hinge

## Slide 4: Engineering Limitation
Plastic Hinge
Pivot Hinge
Minimal Structure
Problems In Real World
1. Plastic has weaker tensile strength than metal
2. Easy to install and design
Design Elements and Analysis Points
Optimized Design by using FEM
Hinge with External Pivot

## Slide 5: Our Product
Parts
Mechanism
This hinge requires a wall that can be mounted above and below the door for installation. This movement is limited to 180 degrees, reducing the constraints to consider.
Hinge X 2
Pin X 1
- Meged View -

## Slide 6: Product Specification
Base Metal |  | ABS Plastic, Z-Ultrat (Tensile Strength 6091 psi)
Size |  | 140mm X 90mm
Thickness |  | 38mm
Hold position |  | 0, almost 180
Bearing |  | Plain bearing with a straight pin
Supported Door | Weight | 13kg (ABS Panel) ~ 39 kg (only Wood)
 | Size | 700mm X 2000mm ~ 1000mm X 2100mm
Hole Pattern |  | Crescent shaped patterns
Screw Type |  | Wood screws, which comes in either a wood boring “fly-cut” variety or in a coarse thread
Maximum Spec
that we test
Base Metal | Steel or ABS Plastic, Z-Ultrat
Main Parts (X 2)
Pin (X 1)

## Slide 7: Engineering Process
The analysis was performed using FEM with Simple Hinge. In FEM, the heaviest and largest door in the current spec was analyzed. Its size and weight are 39 Kg, 1000mm x 2100mm. We used the FEM function of the Inventor and gave it the material properties of the Z-Ultrat ABS plastic hinge.
As a result of this, we identified the concentrated and unnecessary parts around the pin. Finally, topological optimization was performed using a shape generator of Inventor.
FEM
Topological Optimization

## Slide 8: Redesign and Results Analysis
The hinge was redesigned based on the results of applying FEM and Topological Optimization. The results of analyzing our parts are shown on the left.
In the old design, the load was concentrated in the hole and 0.5714 Mpa was the maximum value. However, the redesigned part has no red zone appearing in the hole, and the maximum value is 1.131 MPa, improving performance.
Red zone appears
Max Tensile = 0.517 MPa
No Red Zone
Max Tensile = 1.131 MPa

## Slide 9: DfAM Process and Advantage
Advantage with DfAM
Due to the curved structure, it is difficult to produce using conventional methods. However, with 3D Printing, we can create a very economical hinge.
Because it is plastic and easy to install even if it affects durability, you can print and use it again at home.
Production Point
Since the DfAM method is a non-continuous lamination method, it may exhibit very low lamination strength. So, we have Parts in the same direction as the force when printing.
2. The durability may be weaker than the existing hinge, but it can be used at a cycle similar to that of the other. Rather, it can be used longer because there is no deformation caused by foreign substances.
3. Parts except pins are the same parts. It is compatible, so replacement cost due to component damage is low.